## Slide 1
C-DOT · UPF CONTROL-ROOM LAB · 28TH 11:30–13:00
You are the
network controller.
A stadium surge is approaching. Choose before you see the result.
UPF-A
UL headroom 42
UPF-B
UL headroom 96
UPF-C
UL headroom 131
STADIUM
SURGE
A
Keep static
B
React after overload
C
Steer predictively
Vote now. We reveal the matched result at minute 72.
Synthetic, deterministic simulation · no live C-DOT actuation
01

## Slide 2
WORKSHOP CONTROL LOOP
One causal loop—from observed pressure to later evidence
SYNTHETIC DATA
02 · SYSTEM STORY
01
TRAFFIC
event + offered demand
›
02
SIMULATE
carried · overload · loss
›
03
FORECAST
closed history · p50/p90
›
04
CERTIFY
eligibility · capacity · gate
›
05
STEER
future sessions only
›
06
MEASURE
later telemetry + evidence
‹
realized outcome becomes closed history for the next decision
Participant workspace
Produces a WorkshopDecision record. It has no presenter credentials and cannot publish policy.
Authoritative presenter runtime
Translates one team recommendation into controlled dashboard inputs and records the causal run.
workshop/CDOT_UPF_Closed_Loop_Lab.ipynb · demo_api/runtime.py · steering/policy.py
02

## Slide 3
TRAFFIC SEMANTICS
Demand is what arrived—not only what the network managed to carry
SYNTHETIC DATA
03 · TRAFFIC → SIMULATE
OFFERED
CARRIED
OVERLOAD
+ LOSS
OFFERED
attempted session demand
CARRIED
successfully transported
OVERLOAD
above service envelope
LOSS
offered but not carried
If you train demand on carried throughput during constraint, the label hides the demand you most need to predict.
Notebook TODO 1 · offered, carried, overload and loss remain separate
03

## Slide 4
FORECAST CHOICE
Forecast from closed history; choose how much uncertainty to carry
SYNTHETIC DATA
04 · FORECAST
t−5
166
t−4
174
t−3
181
t−2
188
t−1
196
t−0
204
›
TARGET t
p50
185
p90
222
SOURCE WINDOW ENDS HERE
TARGET STARTS HERE
p50
central estimate · less reserve
p90
conservative · more headroom
No guarantee
unannounced surge may miss both
Forecast/1.0 enforces source_window_end ≤ target_window.start · Notebook TODO 2
04

## Slide 5
POLICY CERTIFICATION
A useful recommendation is still rejected unless it is safe to publish
SYNTHETIC DATA
05 · CERTIFY / OPTIMIZE
✓
CAUSAL
features stop before target
✓
ELIGIBLE
group + locality path exist
✓
HEALTHY
unavailable UPFs get no weight
✓
NORMALIZED
finite [0,1] · sum exactly 1
✓
CAPACITY
UL · DL · session envelope
✓
ANCHORED
new sessions only
INVALID / UNSAFE
Reject recommendation · preserve last safe/static policy
›
VALID
Publish weights for sessions arriving after activation
schemas/policy.py · steering/policy.py · Notebook TODO 3 + required safety drill
05

## Slide 6
MATCHED EVIDENCE
The frozen campaign clears the demo gate—and keeps tail risk visible
SYNTHETIC DATA
06 · REVEAL + COMPARE
MEAN-PAIR UL
+10.52%
95% CI 4.81–16.93%
WEIGHTED UL
+2.84%
severity-weighted total
MATCHED PAIRS
30
static vs frozen MPC
WORST PAIR
−23.50%
fault-heavy regression
AGGREGATE GAIN / WORST PAIR
Demand surge
+10.42%
worst +2.57%
Scheduled fault
+19.01%
worst -23.50%
Unannounced outage
+0.71%
worst -9.84%
Mixed stress
+1.92%
worst -8.28%
Say this
Reduced modeled exposure for future sessions.
Not overload prevented.
Not production ready.
demo_api/data/cohort_mpc_full_campaign_evidence_v1.json · frozen profile and checksums
06

## Slide 7
INTEGRATION BOUNDARY
The next step is a bounded C-DOT advisory pilot—not autonomous control
SYNTHETIC DATA
07 · C-DOT CO-DESIGN + CLOSE
PROMETHEUS
metrics · labels · quality
›
CALIBRATE
UL/DL/session envelopes
›
ELIGIBILITY
slice · DNN · locality
›
SMF HOOK
new-session selection
›
PUBLISH
auth · atomicity · audit
›
ROLL BACK
expiry · last safe policy
RECOMMENDED PILOT SEQUENCE
map telemetry → calibrate capacity → advisory replay → shadow recommendations → bounded new-session pilot
We would deploy this in advisory mode only after ________________________________.
Observe → predict → certify → steer future sessions → measure
07