## Slide 1
C-DOT · PREDICTIVE USER PLANE
Predictive UPF Steering
Simulation to Working Demo
Data modelling, forecasting, controller experiments and evidence
Concise technical review · 09 August 2026
01
MODEL
traffic + events
›
02
GENERATE
30 s simulation
›
03
FORECAST
10–80 min
›
04
OPTIMIZE
2 h cohort MPC
›
05
STEER
new sessions
›
06
DEMO
evidence + outcome
Synthetic, reproducible and explicitly outside a production-release claim.
Implementation + documentation + frozen experiment review
01

## Slide 2
EXECUTIVE SUMMARY
A complete predictive steering loop is implemented and measurable
SYNTHETIC DATA
TRAINING DATA
1.55M
group × 10-minute rows
FORECAST WAPE
7.63%
held-out macro mean
MEAN-PAIR UL GAIN
10.52%
30 matched scenarios
WEIGHTED UL GAIN
2.84%
tail-sensitive total
01 · Traffic model
zones, services, probability and faults
02 · Synthetic history
30-second causal cohort simulation
03 · Forecaster
demand and uncertainty by group
04 · Controller
cohort MPC certified against static
05 · Steering
weighted placement for future sessions
06 · Demo
actual outcomes and frozen evidence
Claim: reduced modeled overload exposure for future sessions—not guaranteed prevention, migration or live C-DOT actuation.
README.md · docs/extreme-forecaster-v1-results.md · docs/cohort-mpc-full-campaign-results.md
02

## Slide 3
SIMULATION DATA · MODELLING
Stage 1 — model diverse traffic as controllable groups
SYNTHETIC DATA
Dimensions
ZONES
8
urban · airport · stadium · industrial · rural
GROUPS
96
zone × DNN × slice × 5QI
12 SERVICE CLASSES
Consumer video
Social/live
Gaming
IMS voice
Enterprise
Video conference
Industrial URLLC
Massive IoT
Connected vehicle
Edge AI
Cloud backup
Public safety
Executable probability model
N(g,t) ~ Poisson(λg × Fg,t)
Fg,t = daily curve × weekend factor × weekly noise × surge multiplier
independent SHA-derived arrival and lifetime streams
uniform integer session lifetime by class
fixed class-level UL/DL Mbps per active session
sessions retained as anchored cohorts after placement
5QI is forecast/QoS metadata, not a separate v1 steering key
configs/extreme_training_profile.json · simulator/macro/engine.py · docs/extreme-data-spec-and-cdot-gap-analysis.md
03

## Slide 4
SIMULATION DATA · EXPERIMENTS
Stage 1 — generate normal regimes, stochastic surges and network stress
SYNTHETIC DATA
DAILY / WEEKLY
258,048 factors
service curves + weekend + U(0.86,1.16)
FLASH CROWDS
192 episodes
12/week · random group · 2–10 h · ×2.5–8
BROWNOUTS
128 episodes
8/week · UL capacity ×0.18–0.70
NEAR OUTAGES
48 episodes
3/week · degraded + 1% capacity
LATENCY
80 episodes
5/week · +25–140 ms
16-week corpus
112 days
322,560 ticks
16,128
10-minute buckets
1,548,288
group observations
24 UPFs
16 edge · 4 regional · 4 central
≈4.39 B
projected session arrivals
≈9.6 GiB
projected artifact volume
Outputs: run.parquet, group/UPF buckets, selection audits and hashed metadata.
Boundary: no mobility, persistent UE identity, heavy-tailed rates, packets or generated telemetry faults in the extreme profile.
experiments/build_extreme_history_manifest.py · docs/extreme-data-spec-and-cdot-gap-analysis.md §§3–8
04

## Slide 5
FORECASTER · TRAINING
Stage 2 — transform the history into causal demand forecasts
SYNTHETIC DATA
30 s data
20 rows
›
10 min bucket
arrivals + mean residual
›
Observation
sessions · UL · DL
›
Direct models
8 horizons
›
Calibration
p50 · p90 · p95
›
Bundle
checksum + metrics
Model
Calendar-ridge direct multi-horizon
96 groups × 3 targets × 8 horizons = 2,304 models
last, MA(6), trend, daily lag and calendar Fourier features
70% train · 15% calibration · 15% chronological test
median bias correction + split conformal uncertainty
Training optimizations
vectorized O(n) feature construction
RMS scaling for national-scale numerical stability
immutable JSON bundle with internal SHA-256
adaptive conformal alpha after realized coverage
3:03 total · ~13 s fitting · ~1.8 GiB RSS
experiments/train_forecaster.py · forecasting/bundle.py · docs/extreme-forecaster-v1-results.md
05

## Slide 6
FORECASTER · EVALUATION
Stage 2 — forecasting beats causal baselines, but surges remain difficult
SYNTHETIC DATA
Held-out WAPE by horizon
0%
4%
8%
12%
10m
4.5
20m
6.1
30m
7.3
40m
8.0
50m
7.4
60m
7.6
70m
9.3
80m
10.7
Overall p90 coverage 94.21% · p95 coverage 96.69%
Baseline comparison
Calendar ridge
7.63%
Daily seasonal
13.71%
MA(6)
14.30%
44.36% WAPE reduction vs seasonal naive
NORMAL
6.51% WAPE
94.19% p90
SURGE
11.08% WAPE
30.73% p90
BROWNOUT
5.09% WAPE
87.88% p90
OUTAGE
5.29% WAPE
73.96% p90
docs/extreme-forecaster-v1-results.md · docs/extreme-optimizer-tuning-results.md
06

## Slide 7
OPTIMIZER · EXPERIMENT PROGRESSION
Stage 3 — experiments showed why a one-window optimizer was not enough
SYNTHETIC DATA
EXPERIMENT
WHAT CHANGED
RESULT / DECISION
One-day predictive pilot
trained p95 forecast + one-window HiGHS LP
+2.40% UL area; insufficient for campaign
Eight-profile tuning
gate, costs, safety factors and static blends
all validation profiles lost to static
Mechanism isolation
scheduled hints, anomaly, lifetime and concentration cap
lifetime helped, but no profile passed
Oracle action-space bound
full-day cohort survival + perfect fault knowledge
100% modeled UL reduction was feasible
Cohort MPC development
two-hour state transition + static certificate
~25.09% mean on five dev seeds
First 12-pair pilot
broader surge/fault/outage/mixed matrix
failed: 4.74% mean; profile rejected
Frozen MA6 MPC
50% static blend + unknown-fault fallback
advanced to fresh 30-pair campaign
Lesson: placements persist for hours; optimizing only the next bucket can create residual concentrations that later decisions cannot undo.
docs/extreme-optimizer-pilot-results.md · extreme-optimizer-tuning-results.md · extreme-oracle-bound-results.md · cohort-mpc-pilot-results.md
07

## Slide 8
OPTIMIZER · CURRENT CONTROL LOOP
Stage 3 — the accepted controller plans cohorts, certifies the action and steers new sessions
SYNTHETIC DATA
CLOSED HISTORY
causal MA(6) p95
›
COHORT STATE
UPF + remaining lifetime
›
2 h MPC
12 future windows
›
STATIC REPLAY
same state + events
›
CERTIFICATE
no worse guardrails
›
FIRST ACTION
publish or exact static
Frozen MPC profile
12 × 10-minute receding horizon
exact anchored cohort state and expected survival
known future capacity path only after known_at_step
50% optimized action + 50% contemporaneous static
fallback to static during unplanned capacity state
UL, DL, drop and session guardrails
How steering works
MPC outputs normalized weights per traffic group and eligible UPF.
Unhealthy or ineligible destinations are removed and weights renormalized.
Each arriving session uses deterministic weighted rendezvous hashing.
Admission checks the selected UPF session limit.
The session stays anchored until its lifetime ends—no migration.
optimization/cohort_mpc.py · simulator/macro/controllers.py · simulator/macro/engine.py · steering/hashing.py
08

## Slide 9
OPTIMIZER · FINAL EVALUATION
Stage 3 — the 30-pair campaign passes the demo gate, with visible tail risk
SYNTHETIC DATA
MEAN-PAIR UL
+10.52%
95% CI 4.81–16.93%
WEIGHTED UL
+2.84%
total overload area
UL DROPPED
+12.42%
aggregate reduction
DL DROPPED
+9.34%
aggregate reduction
AGGREGATE UL OVERLOAD-AREA REDUCTION
Demand surge
8 pairs
+10.42%
Scheduled fault
8 pairs
+19.01%
Unannounced outage
7 pairs
+0.71%
Mixed stress
7 pairs
+1.92%
Tail and release boundary
Worst pair: −23.50%
all aggregate directional guardrails pass
fault-heavy individual regressions remain
working demo candidate—not production-ready
docs/cohort-mpc-full-campaign-results.md · demo_api/data/cohort_mpc_full_campaign_evidence_v1.json
09

## Slide 10
END-TO-END LOOP
From incoming data to a steering decision: one causal 10-minute iteration
SYNTHETIC DATA
01
Collect
30-second class arrivals and per-UPF sessions, UL/DL, capacity, health and quality
02
Close bucket
aggregate 20 ticks; history becomes available only after the window closes
03
Forecast
estimate future new-session demand and upper uncertainty by controllable group
04
Optimize
project anchored cohorts and future arrivals across the 12-window capacity path
05
Certify
compare MPC with static from the identical state and retain static on any failure
06
Steer + observe
new sessions use certified weights; realized placement and loss return as the next history
The dashboard displays this same loop; it does not substitute a prerecorded result for the live causal state.
simulator/macro/engine.py · experiments/train_forecaster.py · optimization/cohort_mpc.py · demo_api/runtime.py
10

## Slide 11
WORKING DASHBOARD
The demo focuses on traffic pressure, steering and evidence
SYNTHETIC DATA
LIVE STATE
UPF load, capacity, health, headroom and loss
STEERING PROOF
previous vs candidate weights and actual new-session placement
FORECAST CHECK
p50/p90 versus realized class demand
EVIDENCE
30-pair metrics, scenario tails and release boundary
frontend/tests/demo.spec.ts-snapshots/ · docs/presenter-guide.md
11

## Slide 12
WORKING DEMO · WALKTHROUGH
A short guided scenario explains what changes—and what does not
SYNTHETIC DATA
STEP
AUDIENCE SEES
INTERPRETATION
1 · Normal
all UPFs inside safe envelopes
existing sessions are anchored
2 · Pressure
class demand rises; capacity threat becomes visible
forecast inputs are still causal
3 · Predict
future demand + same-state static comparison
forecast estimates; MPC chooses
4 · Divert
future-session route widths change
weights change, not existing sessions
5 · Result
actual placement, error, loss and frozen campaign
reduced exposure—not perfect prevention
Key language: ‘future sessions redirected’ and ‘modeled exposure reduced’; never ‘traffic migrated’ or ‘overload prevented.’
docs/presenter-guide.md · demo_api/story.py · demo_api/runtime.py
12

## Slide 13
INTEGRATION BOUNDARY
What is ready today—and what C-DOT must provide for a calibrated pilot
SYNTHETIC DATA
Ready in the repository
deterministic multi-class traffic and fault simulation
canonical artifacts and reproducible experiment evaluation
forecast bundle with uncertainty and causal inference
static-certified cohort MPC and safe fallback
new-session-only simulated steering
working evidence-oriented dashboard
Needed from C-DOT / testbed
live telemetry names, labels, quality and counter semantics
measured directional and session capacity envelopes
real topology, locality and UPF eligibility rules
authenticated SMF/EMS policy publication interface
decision on established-session migration capability
shadow evaluation, untouched release seeds and tail gate
Recommended sequence: map telemetry → calibrate capacities → advisory replay → shadow recommendations → bounded new-session pilot.
docs/extreme-data-spec-and-cdot-gap-analysis.md · docs/cdot-session-migration-decision.md · docs/end-to-end-runbook.md
13

## Slide 14
CONCLUSION
The evidence supports a credible working demo and a clear next pilot
SYNTHETIC DATA
Model the traffic.
Forecast the pressure.
Certify before steering.
The strongest result is not one headline number—it is an end-to-end loop whose assumptions, experiments, gains and limitations remain traceable.
EVIDENCE SNAPSHOT
112-day synthetic history
7.63% forecast WAPE
10.52% mean-pair UL gain
2.84% severity-weighted gain
all aggregate guardrails pass
fault-tail robustness still open
new-session steering only
Proposed discussion
Which C-DOT telemetry and actuation interfaces can support a calibrated shadow pilot?
C-DOT predictive UPF steering · concise technical review
14