## Slide 1
C-DOT · PREDICTIVE USER PLANE
Predictive UPF Steering
Simulation, Forecasting, Optimization & Demo
Implementation review and evidence-backed technical presentation
Prepared for academic review and the C-DOT team · 09 August 2026
01
SIMULATE
30 s causal cohorts
›
02
FORECAST
10–80 min demand
›
03
OPTIMIZE
2 h cohort MPC
›
04
STEER
new sessions only
›
05
DEMONSTRATE
live operator view
All performance evidence in this deck is synthetic and artifact-backed.
Repository review · implementation + docs + frozen experiment artifacts
01

## Slide 2
EXECUTIVE SUMMARY
The system works end to end—and the evidence boundary is explicit
A complete synthetic loop is implemented; the controller is a working demo candidate, not a production release.
SYNTHETIC DATA
TRAINING CORPUS
1.55M
group × 10-minute observations
FORECAST WAPE
7.63%
macro held-out, 10–80 min
MEAN-PAIR UL GAIN
10.52%
30 matched static/MPC pairs
SEVERITY-WEIGHTED GAIN
2.84%
tail risk still material
What is implemented
Deterministic synthetic data factory
30-second cohort simulation, 8 zones, 12 services, 24 UPFs, seeded surges and faults.
Trained probabilistic forecast bundle
2,304 direct calendar-ridge models with p50/p90/p95 conformal envelopes.
Causal cohort-state MPC
Twelve 10-minute windows, persistent-session state, static anchoring, same-state certificate and fallback.
Working dashboard demo
FastAPI + React, REST/WebSocket snapshots, class telemetry, per-UPF routing proof and frozen evidence.
Decision boundary
The accepted claim is reduced modeled overload exposure for future sessions—not guaranteed overload prevention.
Worst paired scenario: −23.50%
No established-session migration
No live SMF/EMS actuation
C-DOT telemetry and capacity calibration remain external
docs/extreme-forecaster-v1-results.md · docs/cohort-mpc-full-campaign-results.md · README.md
02

## Slide 3
EVIDENCE STANDARD
Review basis: implementation, documentation, artifacts and executable checks
SYNTHETIC DATA
01
Implementation
Simulator, forecasting, optimization, steering, API and React UI traced to source.
02
Design records
Architecture decisions, runbooks, traffic specification and C-DOT gap analysis reconciled.
03
Frozen results
Forecast bundle, optimizer tuning, oracle bound and 30-pair campaign evidence reviewed.
90 / 90
backend tests passed
contracts and telemetry reconstruction
deterministic simulator and Parquet
forecast leakage and bundle integrity
HiGHS, cohort MPC and oracle bounds
API, story, rewind and campaign evidence
6 / 6
demo preflight gates passed
traffic registry
3-UPF / 6-class scenario
forecast bundle checksum
FastAPI OpenAPI: 20 paths
production-built operator console
frontend bundle checksum
Evidence rule
Synthetic values, workstation benchmarks and external integration assumptions are never mixed into a production claim.
The worktree is currently dirty; frozen artifacts preserve hashes and exact code identities where documented.
env/bin/python -m unittest discover -s tests -v · env/bin/python scripts/preflight.py
03

## Slide 4
ARCHITECTURE
The implementation is an artifact-backed, causal closed loop
SYNTHETIC DATA
SCENARIO
Seeded manifest
+ topology + events
›
SIMULATE
30 s cohorts
+ traffic accounting
›
AGGREGATE
20 ticks →
10 min observations
›
FORECAST
p50 / p90 / p95
1–12 windows
›
OPTIMIZE
Cohort-state MPC
+ static certificate
›
ACTUATE
Weighted rendezvous
new sessions only
OFFLINE
LIVE
Artifact factory
PBS or workstation shards publish immutable Parquet, JSONL, selection audits and metadata hashes. The cluster is not required during a demo.
Control decision
At a decision boundary, only closed history and declared known-at events are visible. The first MPC action is compared with static from the identical cohort state.
Presentation runtime
One FastAPI process advances the simulator, emits ordered WebSocket deltas, serves the React console and retains an append-only audit trail.
docs/system-architecture-decisions.md · docs/end-to-end-runbook.md · demo_api/runtime.py
04

## Slide 5
STAGE 1 · SIMULATION DATA
Traffic is modeled by controllable groups—not by anonymous aggregate load
SYNTHETIC DATA
Population and dimensions
ZONES
8
urban · industrial · airport · stadium · rural
SERVICES
12
consumer, enterprise, critical and IoT
GROUPS
96
8 zones × 12 service profiles
ELIGIBLE UPFS
6
2 edge + 2 regional + 2 central
Forecast / QoS key
(zone, DNN, S-NSSAI, 5QI)
5QI is descriptive in v1; it is not assumed to be an independent SMF selection key.
Zone and service diversity
north-urban
south-urban
east-urban
west-urban
industrial
airport
stadium
rural
Why grouping matters
Forecasts remain local to an operationally meaningful class.
UPF eligibility and path latency are enforced per group.
Routing weights can shift one class without assuming every session can reach every UPF.
configs/extreme_training_profile.json · experiments/build_extreme_history_manifest.py · docs/extreme-data-spec-and-cdot-gap-analysis.md
05

## Slide 6
STAGE 1 · PROBABILISTIC MODEL
The executable stochastic model is simple, reproducible and deliberately bounded
SYNTHETIC DATA
N(g,t) ~ Poisson( λg × Fg,t )
Fg,t = daily profile × weekend factor × U(0.86, 1.16) weekly noise × active surge
Factors update hourly; arrivals are drawn every 30 seconds.
Determinism by construction
manifest seed fixes events
SHA-256-derived random stream per group
independent arrival and lifetime streams
same seed + policy ⇒ same logical run
SESSION LIFETIME
Discrete uniform integer draw within each class range.
SESSION RATE
Fixed UL/DL Mbps per active session for a class.
STATE
Placed sessions become aggregate cohorts with explicit departure steps.
LOAD
Offered demand is the sum of fixed rates for all active sessions.
Not implemented in the extreme generator: AR(1), Markov bursts, heavy-tailed rate/lifetime, persistent UE identity, mobility, packet-level traffic or telemetry faults.
simulator/macro/engine.py::_poisson · configs/extreme_training_profile.json · docs/traffic-model-spec.md
06

## Slide 7
STAGE 1 · TRAFFIC CATALOG
Twelve service classes create distinct temporal and directional demand
Values are per active session; lifetime ranges are from the executable extreme profile.
SYNTHETIC DATA
SERVICE / DNN
5QI
ARRIVALS / 30 s / ZONE
LIFETIME
UL / DL Mbps
CALENDAR
Consumer video
9
201.6–403.2
1–12 h
0.15 / 4.00
Evening
Social / live
8
112.0–224.0
10 m–2 h
2.00 / 1.00
Evening
Gaming
3
134.4–268.8
40 m–6 h
0.20 / 0.40
Late
IMS voice
1
89.6–179.2
10 m–4 h
0.08 / 0.08
Commute
Enterprise
7
112.0–224.0
30 m–8 h
1.00 / 2.00
Business
Video conference
2
89.6–179.2
30 m–6 h
1.50 / 1.50
Business
Industrial URLLC
82
67.2–134.4
4–24 h
0.10 / 0.08
Industrial
Massive IoT
9
224.0–448.0
6–48 h
0.020 / 0.004
Flat
Connected vehicle
84
112.0–224.0
5 m–1 h
0.50 / 1.00
Commute
Edge AI
7
56.0–112.0
10 m–2 h
3.00 / 6.00
Business
Cloud backup
9
22.4–44.8
1–12 h
8.00 / 2.00
Overnight
Public safety
65
33.6–67.2
20 m–3 h20
2.00 / 2.00
Flat
The same arrival count drives sessions, UL and DL via fixed class rates; identical target WAPE does not imply three independent traffic processes.
configs/extreme_training_profile.json · docs/extreme-data-spec-and-cdot-gap-analysis.md §4
07

## Slide 8
STAGE 1 · SCENARIO CATALOGUE
Scenario generation covers normal regimes, random surges and network disturbances
SYNTHETIC DATA
DAILY / WEEKLY
258,048 factors
service curve × weekend × group/week noise
demand seasonality
FLASH CROWDS
192 episodes
12/week · random group · 2–10 h · ×2.5–8.0
localized step surges
BROWNOUTS
128 episodes
8/week · 1–8 h · UL ×0.18–0.70
capacity, queue, drops
NEAR OUTAGES
48 episodes
3/week · 1–4 h · degraded + 1% capacity
severe residual stress
LATENCY
80 episodes
5/week · 1–6 h · +25–140 ms
path-cost disturbance
Surge IDs are not stored in run.parquet; their multipliers are folded into hourly arrival-factor events. Fault effects appear as resulting UPF state.
experiments/build_extreme_history_manifest.py::_surges/_fault_events · docs/extreme-data-spec-and-cdot-gap-analysis.md §6
08

## Slide 9
STAGE 1 · UPF TOPOLOGY
Eligibility and directional safety envelopes constrain every placement
SYNTHETIC DATA
24-UPF logical hierarchy
One traffic group sees exactly six eligible destinations
ZONE
north
south
east
west
industrial
airport
stadium
rural
EDGE
2 per zone
→
REGIONAL
4 total
→
CENTRAL
4 total
→
Per-instance capacity envelope
TIER
COUNT
UL
DL
SESSION CAP
SAFE
Edge A
8
480 G
1.44 T
1.44 M
78% / 82%
Edge B
8
560 G
1.28 T
1.44 M
78% / 82%
Regional
4
1.12 T
2.40 T
3.52 M
80% / 85%
Central
4
1.92 T
3.84 T
5.12 M
75% / 85%
TOTAL
24
20.48 T
46.72 T
57.60 M
mixed
Admission filters: health ∈ {healthy, degraded} · group eligible · locality path exists · optional max latency · session capacity available.
experiments/build_extreme_history_manifest.py::_upfs/_eligible_upfs · simulator/macro/config.py
09

## Slide 10
STAGE 1 · SIMULATOR MECHANICS
Each 30-second tick preserves causal order and all traffic accounting states
SYNTHETIC DATA
1
CLOSE
At a 10-minute boundary, close the prior 20-tick history bucket.
2
EVENTS
Apply arrival, capacity, health and latency events for this tick.
3
POLICY
Replan if due using current state and only causal history.
4
ARRIVALS
Draw exact Poisson arrivals per group from independent streams.
5
SELECT
Filter eligible/healthy UPFs and run weighted rendezvous per session.
6
ADMIT
Check session capacity; draw uniform lifetime and create a cohort.
7
SERVE
Apply capacity, queues and drops separately for UL and DL.
8
EMIT
Write step telemetry, audit samples and boundary group/UPF state.
Traffic is recorded as offered → carried / queued / dropped, while admission failures and unplaced rejections remain separate.
simulator/macro/engine.py::Simulator.advance · simulator/macro/model.py · steering/hashing.py
10

## Slide 11
STAGE 1 · DATASET AND ARTIFACTS
The 16-week extreme campaign is large enough to stress the full offline path
SYNTHETIC DATA
DURATION
112 d
322,560 × 30-second ticks
TRAINING ROWS
1.548 M
96 groups × 16,128 buckets
PROJECTED SESSIONS
4.39 B
routed arrivals; audit sampled 1:5,000
ARTIFACTS
≈9.6 GiB
one 112-day extreme shard
ARTIFACT
GRANULARITY
WHAT IT PROVES
run.parquet
1 row / 30 s
group arrivals + nested per-UPF UL/DL/session state
group_upf_buckets[]
10 min boundary
joint class/UPF active, admitted and rejected state
selection-audits.parquet
1 / 5,000 sessions
hashed key, eligible set, weights and selected UPF
run.jsonl
readable adapter
metadata + steps + retained selection audits
metadata.json
1 / shard
hashes, source identity, host/job and aggregate metrics
forecast bundle
1 immutable JSON
2,304 models, metrics, calibration and checksum
Measured one-day calibration: 5:06 wall time · 588 MiB peak RSS · 87.6 MiB output. A 112-day shard projects to ~9 h 32 m and ~64 GiB retained memory.
docs/extreme-data-spec-and-cdot-gap-analysis.md §§3,8 · simulator/macro/engine.py::write_parquet
11

## Slide 12
STAGE 2 · FORECASTER TRAINING
Training converts canonical 30-second Parquet into leakage-safe direct forecasts
SYNTHETIC DATA
20 TICKS
sum group arrivals
›
10 MIN
mean UPF residual state
›
OBSERVATION
sessions + UL + DL
›
DIRECT MODELS
3 targets × 8 horizons
›
CONFORMAL
p50 + p90 / p95 widths
›
BUNDLE
checksum + metadata
Exact training row
new_session_count = Σ arrivals in the 20 ticks
new UL/DL = count × fixed class Mbps/session
residual sessions and offered Mbps = duration mean across the bucket
one DemandObservation emitted per controllable group
What the v1 trainer does not consume
queue, drop or rejection fields as targets
selection audits or explicit event IDs
packet counters, CPU, memory or resets/gaps
per-group measured carried throughput
experiments/train_forecaster.py::_bucket_sequence · forecasting/bundle.py
12

## Slide 13
STAGE 2 · MODEL AND TRAINING OPTIMIZATIONS
The chosen forecaster favors transparency, speed and numerical stability
SYNTHETIC DATA
Calendar-ridge direct multi-horizon model
FEATURE
ROLE
last value
autoregressive level
rolling mean (6)
one-hour causal baseline
recent trend
local direction
daily seasonal lag
same-time prior-day structure
sin/cos time of day
continuous daily phase
sin/cos day of week
weekly calendar phase
intercept
group/horizon baseline
96 groups × 3 targets × 8 horizons = 2,304 nine-feature ridge systems
Engineering optimizations
Vectorized row construction
NumPy builds each sequence in O(n); the prior scalar path rebuilt full histories.
RMS feature scaling
stabilizes national-scale normal equations while preserving the bundle coefficient contract.
Ordered split
70% train / 15% calibration / 15% test; features never cross the forecast origin.
Median bias correction
calibration residual median shifts the non-negative p50 point forecast.
Split conformal + ACI
residual widths provide p90/p95; adaptive alpha reacts to realized coverage.
3:03 total · ~13 s fitting · ~1.8 GiB peak RSS · GPU unnecessary for v1
forecasting/bundle.py::_sequence_training_rows/_fit_direct_model · logs/extreme-forecaster-training-optimized.log
13

## Slide 14
STAGE 2 · FORECAST RESULTS
Held-out performance is strong at operational horizons and degrades predictably with lead time
SYNTHETIC DATA
Macro WAPE by horizon
0%
3%
6%
9%
12%
10m
4.48
20m
6.09
30m
7.35
40m
7.95
50m
7.42
60m
7.63
70m
9.34
80m
10.73
p90 upper-bound coverage stays between 93.10% and 94.96% across all eight horizons.
Fair baseline comparison
Calendar ridge
7.63%
Daily seasonal
13.71%
MA(6)
14.30%
44.36% lower WAPE than daily seasonal naive.
docs/extreme-forecaster-v1-results.md §§3–4 · output/models/extreme-forecaster-v1-baseline-evaluation.json
14

## Slide 15
STAGE 2 · REGIME ANALYSIS
Surges—not brownouts—are the dominant forecast weakness
SYNTHETIC DATA
REGIME
WAPE
P90 COVERAGE
INTERPRETATION
Normal
6.51%
94.19%
well calibrated
Surge
11.08%
30.73%
unannounced step-change is not predictable beforehand
Brownout
5.09%
87.88%
network state changes; offered demand does not
Near outage
5.29%
73.96%
demand accuracy stays normal; coverage weakens
Latency incident
5.04%
92.36%
path state changes, not demand
Operational consequence
The controller needs robust fallback and static-relative certification; forecast accuracy alone cannot guarantee benefit.
Evaluation caveat
The v1 70/15/15 split differs slightly from the manifest’s explicit 11/2/3-week boundary; event-stratified release reporting remains incomplete.
docs/extreme-optimizer-tuning-results.md §Forecast performance by regime · docs/extreme-forecaster-v1-results.md
15

## Slide 16
STAGE 3 · CONTROLLER EVOLUTION
The optimizer evolved only after the evidence disproved the first design
SYNTHETIC DATA
01 · ONE-WINDOW LP
p95 forecast + residual load
Validation failed
›
02 · MECHANISM TUNING
hints · anomaly · lifetime · caps
Still worse than static
›
03 · ORACLE BOUND
full-day cohort relaxation
100% modeled UL reduction possible
›
04 · COHORT MPC
12-window state transition
10.52% mean-pair gain
Core lesson
New-session decisions persist for hours. A controller that optimizes only the next bucket can create residual concentrations that it cannot later undo.
The successful redesign carried cohort survival through a two-hour horizon and compared every candidate with static from the same state.
docs/extreme-optimizer-tuning-results.md · docs/extreme-oracle-bound-results.md · docs/cohort-mpc-full-campaign-results.md
16

## Slide 17
STAGE 3 · FAILURE ANALYSIS
Why the one-window HiGHS controller lost to a strong static baseline
SYNTHETIC DATA
Mechanism of failure
Myopic horizon
Minimizing next-window peak utilization ignores the future occupancy of long-lived cohorts.
Persistent placement
Only future sessions are controllable; already placed sessions cannot be rebalanced.
Correlated concentration
A per-group weight cap does not prevent many groups from choosing the same failure domain.
Forecast step-changes
Surge p90 coverage collapses before an unannounced jump becomes observable.
Static is robust
Capacity-weighted rendezvous spreads each group broadly and continuously.
Validation outcome versus static
Responsive gate p95
-7.1%
Static anchor · 10%
-9.1%
Default p95
-39.0%
Load-only aggressive
-76.5%
Load-first · +35% safety
-93.8%
Load-first · +15% safety
-168.0%
No profile passed guardrails; reserved fresh test seeds were preserved rather than used for selection.
docs/static-controller-deep-research.md · docs/extreme-optimizer-tuning-results.md
17

## Slide 18
STAGE 3 · COHORT MPC
Cohort-state MPC plans the consequences of today’s weights across twelve windows
SYNTHETIC DATA
State transition model
Projected load(u,t) = anchored cohorts(u,t) + Σg,τ≤t x(g,τ,u) · demand(g,τ) · survival(g,t−τ)
HORIZON
12 × 10 min = 2 hours
DEMAND
causal MA(6) p95; scheduled multipliers only after known_at_step
STATE
exact active cohorts by group, UPF, remaining lifetime and directional rate
CAPACITY PATH
current state + declared future health/capacity events
DECISION
continuous group→UPF weights for each horizon window
ACTION
only the first window is published; replan every 10 minutes
Frozen demo profile
MAX UPF WEIGHT
0.75
STATIC BLEND
50%
SOLVER TIMEOUT
2.0 s
OVERLOAD COST
1×
PHYSICAL DROP COST
10×
TERMINAL EXPOSURE
1×
UNPLANNED CAPACITY
fallback static
optimization/cohort_mpc.py · simulator/macro/controllers.py::CohortMPCController · configs/cohort_mpc_pilot_10pct_v2.json
18

## Slide 19
STAGE 3 · SAFETY AND FALLBACK
Every MPC action is guarded by a same-state static certificate
SYNTHETIC DATA
1
FORECAST
12-window demand
›
2
SOLVE
HiGHS LP
›
3
REPLAY
static from same state
›
4
CERTIFY
guardrails + gain
›
5
PUBLISH
or exact static
Certificate requires
UL overload area no worse than static
DL overload area no worse than static
session overload no worse than static
UL and DL physical drops no worse than static
minimum score and modeled UL improvement
Fallback triggers
insufficient history or forecast error
solver infeasible / error / timeout
certificate rejects the candidate
observed unplanned capacity state
no healthy eligible route exists
optimization/cohort_mpc.py::_certificate · simulator/macro/controllers.py::_static_fallback · steering/policy.py
19

## Slide 20
STAGE 3 · EVALUATION RESULTS
The frozen 30-pair campaign passes the working-demo gate
SYNTHETIC DATA
MEAN-PAIR UL
+10.52%
bootstrap 95% CI: 4.81–16.93%
SEVERITY-WEIGHTED UL
+2.84%
dominated by highest-overload days
UL DROPPED BYTES
+12.42%
aggregate reduction
DL DROPPED BYTES
+9.34%
aggregate reduction
Exactly paired experiment
30 fresh seeds
34001–34030; one simulated day per pair.
Common random numbers
same scenario, arrivals, lifetimes, event schedule and rendezvous namespace.
Four stress families
8 surge · 8 scheduled fault · 7 unannounced outage · 7 mixed.
Aggregate guardrails
DL overload, both directional drops and establishment failures all pass.
Release decision
Working demo candidate—not production-ready.
WORST MATCHED PAIR
−23.50%
scheduled-fault tail regression
docs/cohort-mpc-full-campaign-results.md · demo_api/data/cohort_mpc_full_campaign_evidence_v1.json
20

## Slide 21
STAGE 3 · SCENARIO BREAKDOWN
Average gains are broad, but robustness is weakest under surprise and fault tails
SYNTHETIC DATA
AGGREGATE UL OVERLOAD-AREA REDUCTION
Demand surge
n=8
+10.42%
Scheduled fault
n=8
+19.01%
Unannounced outage
n=7
+0.71%
Mixed stress
n=7
+1.92%
Worst pair by scenario
Demand surge
+2.57%
Scheduled fault
-23.50%
Unannounced outage
-9.84%
Mixed stress
-8.28%
Next release gate: positive severity-weighted confidence bounds on untouched seeds, plus materially reduced unannounced-outage and scheduled-fault tails.
demo_api/data/cohort_mpc_full_campaign_evidence_v1.json · docs/cohort-mpc-full-campaign-results.md
21

## Slide 22
STAGE 4 · WORKING DEMO
The dashboard is a real causal runtime—not a prerecorded animation
SYNTHETIC DATA
REACT OPERATOR CONSOLE
Live Dashboard · Evidence · Technical Detail · Expert mode
REST + WEBSOCKET
commands and snapshots · ordered versioned deltas · reconnect
FASTAPI ORCHESTRATOR
run lifecycle · auth roles · audit · story checkpoints · analytics
CAUSAL SIMULATION LOOP
30 s tick · 10 min control · forecast · MPC · actuator
FROZEN ARTIFACTS
scenario · forecast bundle · MPC profile · 30-pair evidence
The server chooses the policy before realizing the tick; event injection never rewrites prior telemetry. Rewind restores complete runtime state.
demo_api/main.py · demo_api/runtime.py · frontend/src/App.tsx · docs/system-architecture-decisions.md ADR-021–023
22

## Slide 23
STAGE 4 · DASHBOARD DATA AND FEATURES
The operator sees both the decision and the evidence behind it
SYNTHETIC DATA
LIVE DASHBOARD
per-UPF capacity, load, headroom and health
new-session route widths and weight deltas
forecast → certificate → apply/hold trace
completed surge debrief and iteration ledger
EVIDENCE
30 matched-pair frozen campaign
mean-pair CI and severity-weighted total
scenario-level aggregate and worst pair
artifact identity and production boundary
TECHNICAL DETAIL
class arrivals, admissions and rejections
p50/p90/actual forecast table
static vs MPC certificate metrics
raw trace, deployment boundary and expert controls
DISPLAYED DATA SOURCES
simulator StepResult · canonical group/UPF buckets · Forecast · Policy · certificate · frozen campaign JSON
frontend/src/views.tsx · frontend/src/types.ts · demo_api/runtime.py::snapshot/comparison
23

## Slide 24
STAGE 4 · DASHBOARD EXPERIENCE
The actual console keeps routing, evidence and caveats visible
SYNTHETIC DATA
Predict + compare checkpoint
Route widths encode future-session allocation; the side rail exposes the same-state static comparison and the no-migration caveat.
Frozen campaign evidence
The evidence view leads with the 10.52% average but places severity weighting, worst pair and release status beside it.
frontend/tests/demo.spec.ts-snapshots/prediction-checkpoint-linux.png · evidence-ending-linux.png
24

## Slide 25
STAGE 4 · HOW DIVERSION WORKS
Traffic diversion is deterministic weighted placement for newly arriving sessions
SYNTHETIC DATA
SIMULATOR PLACEMENT PATH
requested = policy_weights[group_id]
allowed = {u:w for u,w in requested.items()
if u in eligible_upfs
and state[u].health in {healthy,degraded}}
weights = normalize(allowed)
selected = rendezvous_select(
session_key, stable_namespace, weights)
if active[selected] >= session_capacity:
reject()
else:
lifetime = randint(min_steps, max_steps)
create_anchored_cohort(selected, lifetime)
The policy ID does not re-salt the hash namespace; paired runs share the selection randomization.
What a weight change means
Before
Each new session hashes across the current eligible weighted set.
Policy epoch
MPC publishes new normalized weights after certification.
After
Only later arrivals use the new weighted scores.
Persistence
Admitted sessions stay on the selected UPF until their lifetime ends.
No migration
Existing TEIDs/sessions are never moved by this code.
simulator/macro/engine.py::advance · steering/hashing.py::rendezvous_select · docs/cdot-session-migration-decision.md
25

## Slide 26
STAGE 4 · PRESENTER WALKTHROUGH
A five-minute guided story makes the control loop explainable
SYNTHETIC DATA
TIME
CHECKPOINT
WHAT THE AUDIENCE SEES
DEFENSIBLE CLAIM
0:00
Normal network
three UPFs inside safe envelopes
established sessions remain anchored
0:35
Problem appears
stadium demand rises; known UPF-A UL reduction
pressure is visible before the route changes
1:20
Predict + compare
causal MA6 forecast + same-state certificate
forecast does not steer traffic by itself
2:35
Divert new sessions
new route widths and per-UPF weight deltas
future arrivals shift; existing sessions do not
3:40
Result + evidence
realized outcome, loss and frozen 30-pair evidence
modeled exposure is reduced, not eliminated
Deterministic checkpoints are server-side state: browser reload, brief disconnect and rewind do not invent or recompute realized history.
docs/presenter-guide.md · demo_api/story.py · demo_api/runtime.py::_guided_story/rewind
26

## Slide 27
QUALITY ASSURANCE
Verification spans contracts, causality, optimization and the presentation surface
SYNTHETIC DATA
CONTRACTS
versioned schemas · round-trip fixtures · normalized policies
CAUSALITY
no future observations · known_at_step enforcement · append-only history
SIMULATOR
deterministic streams · queues/drops · Parquet schema · audit sampling
OPTIMIZER
hand-solvable LPs · eligibility · diversification · same-state certificate
EXPERIMENTS
exact pairing · reserved seeds · immutable outputs · bootstrap interval
DEMO
auth roles · OpenAPI · WebSocket order · rewind exactness · visual snapshots
BACKEND TESTS
90
all passed in 4.56 s
API PATHS
20
FastAPI preflight
VISUAL BASELINES
13
desktop, tablet and mobile
PREFLIGHT
PASS
all data labeled synthetic
tests/ · frontend/tests/demo.spec.ts · scripts/preflight.py · verified 09 Aug 2026
27

## Slide 28
C-DOT INTEGRATION BOUNDARY
Simulation and production integration are intentionally separated
SYNTHETIC DATA
Available now
deterministic cohort simulation and event injection
canonical Parquet, audit and hashed metadata
trained forecast bundle with uncertainty bounds
causal cohort MPC with static certificate
simulated new-session actuation
Prometheus-compatible synthetic metrics
REST/WebSocket operator dashboard
advisory and placeholder actuator interfaces
Requires C-DOT / testbed
live Prometheus metric names, labels and scrape semantics
measured UPF UL/DL/session capacity envelopes
topology, locality and eligibility truth
authenticated SMF/EMS policy publication contract
confirmation of established-session relocation support
free5GC/PacketRusher integration and saturation tests
production drift, missingness and counter-reset behavior
untouched release campaign and tail-risk gate
demo_api/interfaces.py · docs/cdot-session-migration-decision.md · docs/extreme-data-spec-and-cdot-gap-analysis.md §§11–13
28

## Slide 29
ROADMAP
Recommended path from working demo to C-DOT-calibrated pilot
SYNTHETIC DATA
01
Observe
Map N3/N6 counters, sessions, health and label cardinality into versioned telemetry contracts.
02
Calibrate
Measure directional throughput/session envelopes and reproduce overload thresholds on target UPF builds.
03
Replay
Run the existing forecaster and MPC in advisory mode against recorded representative history.
04
Shadow
Publish recommendations to an external store without actuation; compare static and MPC decisions online.
05
Pilot
Enable bounded new-session steering with fail-closed rollback and explicit operational approval.
Go/no-go principle: calibrate data and authority first; keep the current synthetic evidence intact as a reproducible engineering baseline.
docs/static-controller-deep-research.md §Recommended backlog · docs/end-to-end-runbook.md §Remaining implementation checklist
29

## Slide 30
CONCLUSION
The engineering result is credible because the limitations are visible
SYNTHETIC DATA
Predict early.
Certify against static.
Steer only what is controllable.
The repository demonstrates an end-to-end synthetic control loop with measurable average benefit, reproducible artifacts and an honest production boundary.
FINAL TAKEAWAYS
7.63% forecast WAPE
10.52% mean-pair UL improvement
2.84% severity-weighted benefit
all aggregate guardrails pass
fault-tail risk remains
new-session placement only
Discussion
What telemetry, capacity and actuation interfaces can C-DOT expose for a calibrated shadow pilot?
C-DOT predictive UPF steering · technical review · 09 August 2026
30

## Slide 31
APPENDIX · METRICS
Appendix: metric definitions used in the experiments
SYNTHETIC DATA
METRIC
DEFINITION
WHY IT MATTERS
WAPE
Σ|actual−p50| / Σ|actual|
scale-normalized forecast point error
p90 coverage
fraction where actual ≤ predicted upper p90
uncertainty calibration for conservative planning
UL overload area
Σ max(0, load/safe_capacity−1) × seconds
severity × duration above safe envelope
Overload duration
seconds with load above safe capacity
duration only; ignores magnitude
Dropped bytes
overflow beyond physical capacity and bounded queue
modeled service loss
Establishment failures
sessions rejected by capacity or no eligible route
admission quality guardrail
Mean-pair reduction
mean of per-seed relative reductions
equal weight to each paired scenario
Severity-weighted reduction
reduction in total area across all pairs
weights heavy overload days more strongly
Total variation
½ Σ|new weight−old weight|
policy churn / amount of routing change
The primary supplied-demo metric is directional UL overload area; DL is reported separately and cannot be hidden by a combined average.
forecasting/metrics.py · simulator/macro/engine.py::SimulationResult.summary · experiments/evaluate_cohort_mpc_candidate.py
31

## Slide 32
APPENDIX · TRACEABILITY
Appendix: source map for implementation and evidence review
SYNTHETIC DATA
STAGE
PRIMARY IMPLEMENTATION
PRIMARY EVIDENCE / DOCS
Scenario generation
experiments/build_extreme_history_manifest.py
configs/extreme_training_profile.json
docs/extreme-data-spec-and-cdot-gap-analysis.md
docs/traffic-model-spec.md
Simulator
simulator/macro/engine.py
simulator/macro/config.py · model.py
docs/end-to-end-runbook.md
docs/system-architecture-decisions.md
Forecaster
experiments/train_forecaster.py
forecasting/bundle.py · baselines.py · metrics.py
docs/extreme-forecaster-v1-results.md
One-window LP
optimization/highs.py
simulator/macro/controllers.py
docs/extreme-optimizer-tuning-results.md
docs/static-controller-deep-research.md
Oracle + cohort MPC
optimization/oracle_bounds.py
optimization/cohort_mpc.py
docs/extreme-oracle-bound-results.md
docs/cohort-mpc-full-campaign-results.md
Steering
steering/hashing.py · policy.py · gate.py
docs/cdot-session-migration-decision.md
Working demo
demo_api/main.py · runtime.py · story.py
frontend/src/App.tsx · views.tsx
docs/presenter-guide.md
frontend/tests/demo.spec.ts-snapshots/
Frozen campaign evidence: demo_api/data/cohort_mpc_full_campaign_evidence_v1.json · source SHA-256 bd1d3727…b662c
Repository: /home/prarabdha/work/5g-simulation · deck generated from current workspace state
32