## Slide 1
C-DOT · 5G DIGITAL TWIN · 90-MINUTE CONTROL-ROOM WORKSHOP
You are the
network controller.
A synthetic stadium surge is approaching. Vote before the result is revealed.
A
Keep Static
B
React after overload
C
Steer predictively
JOIN JUPYTERHUB
Open your assigned notebook.
Run Stage 01 preflight.
Reveal at minute 72.
Synthetic simulation · no live C-DOT traffic · no SMF actuation
01

## Slide 2
SCOPE
What this digital twin represents
SYNTHETIC DATA
02 · 90-MINUTE WORKSHOP
REPRESENTS
Synthetic traffic, topology, capacity, telemetry, forecast uncertainty, optimization, policy gates and later evidence.
DOES NOT REPRESENT
Live C-DOT traffic, measured geography, autonomous production control, or established-session migration.
CONTROL SCOPE
Recommendations change only the placement of sessions that arrive after an accepted policy epoch.
Minute 6–14 · participant preflight
02

## Slide 3
READINESS BOUNDARY
Implemented here; external integration remains gated
SYNTHETIC DATA
03 · 90-MINUTE WORKSHOP
IMPLEMENTED
24-UPF/96-group synthetic model · deterministic simulator · HiGHS · policy gate · PBS campaign jobs · dashboard · replay.
CLUSTER-PREFLIGHT
SCIP, PySCIPOpt, ParaSCIP/UG, MPI/PALS and PBS launch syntax must pass on the actual cluster ≥7 days before delivery.
EXTERNAL-PENDING
C-DOT telemetry mapping · calibrated envelopes · security · SMF/EMS future-session hook · publication/rollback runbook.
No silent solver substitution · ParaSCIP readiness failure blocks the live track
03

## Slide 4
END-TO-END LOOP
One causal control loop—from pressure to later evidence
SYNTHETIC DATA
04 · 90-MINUTE WORKSHOP
OBSERVE → FORECAST
Offered demand and quality flags enter a closed-history p50/p90 forecast. Target data never enters features.
OPTIMIZE → CERTIFY
Capacity, eligibility, health, locality and churn gates evaluate a candidate. Unsafe means last-safe/static.
PLACE → MEASURE
Only future sessions use new weights. Carried traffic, overload and loss become later evidence—not rewritten history.
Causal markers are carried into twin-replay/1.0
04

## Slide 5
TOPOLOGY + TRAFFIC
A synthetic national topology creates repeatable stress
SYNTHETIC DATA
05 · 90-MINUTE WORKSHOP
24 UPFs
Heterogeneous UL/DL/session capacity, safe envelopes, health and failure-domain events.
96 GROUPS
Zone × DNN × S-NSSAI demand classes with eligibility and deterministic offered-load generation.
TRAFFIC SEMANTICS
Offered demand is attempted load. Carried is an outcome. Their constrained gap is loss/overload.
Synthetic spatial layout · not C-DOT geography
05

## Slide 6
PBS ARCHITECTURE
The 160-node cluster buys breadth—not one giant simulation
SYNTHETIC DATA
06 · 90-MINUTE WORKSHOP
RIGHT UNIT
One scenario × controller × seed is one bounded one-node, one-CPU PBS job.
CAMPAIGN BREADTH
Independent jobs explore seeds, events, controllers and parameter regimes concurrently across the cluster.
ISOLATION
$USER + PBS job ID + seed identify private outputs. No shared writable participant campaigns.
Minute 14–22 · 24 UPFs · 96 groups · arrays are a scenario factory
06

## Slide 7
CONTINUOUS ALLOCATION
The teaching LP turns demand into safe routing weights
SYNTHETIC DATA
07 · 90-MINUTE WORKSHOP
VARIABLES
xᵤ = new-session Mbps assigned to eligible UPF u · sᵤ = explicit overload slack.
CONSTRAINTS
Σxᵤ = demand · xᵤ ≤ residual capacityᵤ + sᵤ · xᵤ = 0 when ineligible.
OBJECTIVE + OUTPUT
Minimize latency-weighted allocation + severe slack penalty. Normalize wᵤ = xᵤ / demand.
Minute 22–32 · edit demand/capacity · solve with HiGHS
07

## Slide 8
SOLVER + PBS MODEL
SCIP validates the LP; ParaSCIP demonstrates the larger MIP
SYNTHETIC DATA
08 · 90-MINUTE WORKSHOP
INDIVIDUAL
Same LP in HiGHS and SCIP; feasible objectives must agree within tolerance. One-node SCIP job per participant.
WHY A MIP
24-UPF/96-group assignment uses binary group→UPF and UPF-activation variables. The tiny LP cannot teach distributed search.
PRESENTER ONLY
One frozen-seed, two-node ParaSCIP/UG job in a reservation. Participants watch status/result; they never submit ParaSCIP.
Minute 32–52 · strict 4 GB / 5–10 minute ceilings
08

## Slide 9
TRAFFIC ACCOUNTING
Offered demand and carried throughput answer different questions
SYNTHETIC DATA
09 · 90-MINUTE WORKSHOP
OFFERED
What active and newly arriving sessions attempted to transmit—independent of whether capacity served it.
CARRIED
What crossed the modeled service path after capacity, queueing, rejection and drops.
DO NOT CONFUSE
A saturated carried-throughput series can hide true demand. Forecast from offered demand with quality flags.
Minute 52–62 · safety drill while PBS jobs run
09

## Slide 10
CAUSALITY + P50/P90
Forecast uncertainty changes what ‘safe’ means
SYNTHETIC DATA
10 · 90-MINUTE WORKSHOP
CAUSAL INPUT
Only closed windows at or before issue time. Scheduled events enter only when known by then.
p50 vs p90
p50 is central expectation; p90 is a conservative planning quantile—not a guarantee against surprise flash crowds.
MARK EVERY FRAME
Source window, target window, policy apply step and anchored-session marker preserve replay semantics.
Forecasts are synthetic model outputs, not live traffic predictions
10

## Slide 11
POLICY GATE
Certification makes rejection visible and fail-safe
SYNTHETIC DATA
11 · 90-MINUTE WORKSHOP
CHECK
Causality · finite normalized weights · eligibility · health · locality · UL/DL/session headroom · churn.
REJECT
Unknown destination, non-normalized weight, unsafe projection or migration request fails certification.
FALL BACK
Retain last-safe/static policy with reason, status, audit and expiry. Never publish slack or silently switch solvers.
Participant notebooks have neither credentials nor publication access
11

## Slide 12
POSITIVE GUIDED EVIDENCE
The guided three-UPF story is positive within its matched scope
SYNTHETIC DATA
12 · 90-MINUTE WORKSHOP
EVIDENCE SCOPE · Frozen guided three-UPF showcase · 30 matched pairs · positive result
+10.52%
Matched 30-pair guided result in the frozen three-UPF showcase evidence. Present as a scoped modeled improvement.
WHAT CHANGED
Accepted weights changed future-session placement; established sessions stayed anchored.
WHAT IT DOES NOT PROVE
No live-network benefit, no universal overload prevention, no production recommendation.
demo_api/data/cohort_mpc_full_campaign_evidence_v1.json
12

## Slide 13
NATIONAL CONTROL SCIENCE
The later national result does not promote MPC
SYNTHETIC DATA
13 · 90-MINUTE WORKSHOP
EVIDENCE SCOPE · Later national-scale control-science campaign · production decision
LATER EVIDENCE
Broader national-scale campaign evaluates the controller under more regimes and guardrails than the guided story.
DECISION
MPC fails promotion. Static remains the production-safe controller conclusion.
HONEST HANDOFF
The older +10.52% remains useful teaching evidence, but is not the latest production recommendation.
configs/control_science_v1.json · promotion conclusion is authoritative
13

## Slide 14
EXPERIENCE + CLOSE
From dashboard and 3D replay to a bounded advisory pilot
SYNTHETIC DATA
14 · 90-MINUTE WORKSHOP
EXPERIENCE
Presenter dashboard streams the guided story; participant iframe replays completed Parquet in the full Three.js world.
OPERATIONAL GATES
35-user rehearsal · reserved short queue · offline assets · WebGL2 · storage pressure · 90-minute run + 5-minute margin.
C-DOT PATH
Map telemetry → calibrate envelopes → shadow/advisory replay → secure audited future-session pilot → rollback exercise.
Minute 87–90 · export WorkshopReport · close the advisory-pilot sentence
14